Glossary of terms

- NFIS: negative feedback inhibition system. It is composed of a coupled receptor
  and effector in a closed loop
- Effector: component of NFIS – responsible for delivering a product
- Receptor: component of NFIS responsible for controlling an effect. If the programmed
  value of the regulation threshold is reached, the receptor issues a control
  signal, disabling the effector
- External receptor: receptor coupled with another NFIS (considered here as the
  secondary NFIS). Regulation thresholds of NFIS systems may be affected by signals
  from such external receptors, coupling them. Interconnection is mostly realized
  by products of NFIS systems which thus play the role of coupling signals
- Organized systems (OS): all interconnected negative feedback inhibition systems.
- State: concentration of products delivered by effectors.
- Old / previous state: state of the OS, as defined above, during the previous time
  step used to describe a simulation algorithm from a dynamic perspective.

Software model

OS (organized systems)
A single organized systems (OS) entry is composed of:
- NFISs: list of coupled effectors and receptors.
- Receptors: list of external receptors coupled with other NFISs . Each such receptor
  can modify threshold values of coupled NFISs.
- Init: initial state of the OS. Defines concentration of products for the first run of the
  simulation. This is especially important for NFISs with the substrate parameter
  defined. In such cases, some substrate is required for any production. The initial
  concentration of each substrate should be defined in this section.
  An OS also has the following properties:
  - Name: user-defined identification of an OS. Users of the application can load an OS using the name.
  - Description: user-defined description of an OS. The description should elaborate on the purpose of the OS or biological phenomena it models.

NFIS
One Negative Feedback Inhibition System (NFIS) is composed of the following components:
- effector
- receptor
An NFIS has an id property. The id defines a logical name of an NFIS. It is used by the
application in order to uniquely identify an NFIS through a simulation.

Effector
A single effector is characterized by the following properties:
- Product: mandatory – name of the product delivered by this particular effector.
- Substrate: optional – defines a product that should be used as a substrate for this particular effector. The product is delivered by another effector. It is defined as the product parameter’s value. Substrate product exchange means that NFIS systems are connected by cooperation. If the parameter is not defined, the substrate is considered as “always available”. This means that the effector always delivers the exact amount of product molecules as defined by the production parameter.
- Production: mandatory – maximum production rate of the effector defined by the number of molecules per time unit. “Maximum rate” means that if a substrate is available in an amount greater than or equal in relation to the value of the described parameter, the effector delivers exactly the same amount of product.
- Outflow: optional – product outflow rate defined as the number of molecules per time unit. Outflow models diffusion as occurring in biological systems.
Receptor
A single receptor is characterized by the following properties:
- Delay: optional – time required for this particular receptor to become active. If a product threshold is exceeded, a signal of this receptor (coupled) affects the effector only after a defined number of time units. This parameter was introduced to model communication in biological systems, which is rarely immediate.
- Thresholds: mandatory – list of threshold levels (values) defined for this particular receptor. One of the defined values will be used to activate the receptor during simulation. Each threshold value configuration is characterized by the following properties:
  - Signal: optional – defineswhich external receptor becomes active in response to the surpassed threshold value. If this parameter is not defined, the threshold value will always be considered for the receptor’s activation. In other words, this parameter defines the condition under which a value will or will not be considered.
  - Product: mandatory – defines which product is considered when this configuration is active. The considered product’s concentration is checked versus the threshold value. For a proper negative feedback loop there has to be at least one threshold configuration with the value of this parameter equal to the product of coupled effector. If the value of this parameter refers to any other product, it means that there is coordination between this NFIS and the NFIS delivering the product.
  - Value: mandatory – defines the threshold concentration of the product. If it is exceeded for the amount of time defined by the value of the delay parameter, the signal of this receptor becomes active.
External receptor
Single external receptor – receptor coupled with some other NFISs. It differs from a
regular receptor by only one added property: id.